## Slide 1
FL7733 EVT1 System Verification Report
Oct.29.2013
Power Conversion Korea
Inki-Park

## Slide 2: Schematics[8.4W]

## Slide 3
Transformer Core : RM6
Inductance of Primary side : 1mH
No | Winding | Pin(S → F) | Wire | Turns | Winding Method
1 | NP1 | 6 1 | 0.20φ | 54Ts | Solenoid winding
2 | Insulation : Polyester Tape t = 0.025mm, 2Layers |  |  |  | 
3 | NS | NS +  NS- | 0.25φ (TIW) | 30Ts | Solenoid winding
4 | Insulation : Polyester Tape t = 0.025mm, 2Layers |  |  |  | 
5 | NA | 5 3 | 0.16φ | 20Ts | Solenoid winding
6 | Insulation : Polyester Tape t = 0.025mm, 2Layers |  |  |  | 
7 | NP2 | 1  2 | 0.20φ | 27Ts | Solenoid winding
8 | Insulation : Polyester Tape t = 0.025mm, 6Layers |  |  |  | 
Transformer[8.4W]

## Slide 4
1. Protection
1) SCP
2) SRSP
3) SROP
4) ODSP
5) VS OVP

## Slide 5: SCP
Concept
VS voltage at gate-off is close to zero when LED load is shorted.
SCP is disabled for the initial 14 ms once VDD is higher than UVLO.
200ms JFET regulation enlarges AR time during SCP.

## Slide 6: SCP
Test Results
SCP de-bounce cycle is 4 and operated well.
Test condition: CCOMI[2.2uF], CVDD[10uF].
Vin[90Vac]
Ch1[VGATE],,Ch2[VIN], Ch3[VVS], Ch4[IOUT]
Vin[265Vac]

## Slide 7: SCP
Test Results
TSCP.bnk of EVT1 was larger than EVT0.
JFET regulation is operated well.
Test condition: , Rstr[30k], CCOMI[1.0uF], CVDD[10uF].
TSCP.bnk:14ms -->OK
Ch1[VDD],,Ch2[VIN], Ch3[VGATE], Ch4[IOUT]
EVT0
Ch1[VGATE],,Ch2[VIN], Ch3[VDD], Ch4[IOUT]
EVT1
TSCP.bnk:16ms
VJFET.HL : 19V
VJFET.LL : 13V

## Slide 8: Current-mode SRSP
Current-mode SRSP protects the condition that sensing resistor is short before VDD-ON.
Vin level is be detected by Ivs and TVCS-BNK is inversely proportional to Vin level.
Once VCS is maintained under 0.1V for TVCS-BNK, SRSP is triggered.
Current-mode SRSP is monitored only for first switching cycle.
Concept

## Slide 9: Current-mode SRSP
Test Results
SRSP is operated well.
JFET regulation is operated well.
Test condition: CCOMI[2.2uF], CVDD[10uF].
TonSRSP: 4.2us
VJFET.HL : 19V
Vin[90Vac]
Vin[265Vac]
Vin[265Vac]
Ch1[VDD],,Ch2[VIN], Ch3[VCS], Ch4[IOUT]
TonSRSP: 1.9us
VJFET.LL : 13V

## Slide 10: Voltage-mode SRSP
Voltage-mode SRSP protects the condition that sensing resistor is short after VDD-ON.
SRSP monitoring is enabled when Vin is higher than 60% of peak Vin.
Once VCS is maintained under 0.1V for SRSP monitoring time, SRSP is triggered.
Concept

## Slide 11: Voltage-mode SRSP
Test Results
Voltage mode SRSP is operated well
Test condition: CCOMI[2.2uF], CVDD[10uF].
Vcs < 0.1V
Rcs Short
Ch1[VDD],,Ch2[VGATE], Ch3[VCS], Ch4[IOUT]
a
b
a
b
Rcs Short
SRSP Trigger
Vin: a<b
Vcs: a>b
A
B
A
B
Vin: a<b
Vcs: a>b
Vin: 83V[≈130V *0.6]
Vin: 248V[≈368V *0.6]
Vcs < 0.1V
SRSP Trigger
Vin[265Vac]
Vin[90Vac]

## Slide 12: SROP
Test Results
SROP is operated well.
JFET regulation is operated well.
Test condition: CCOMI[2.2uF], CVDD[10uF].
Ch1[VGATE],,Ch2[VDD], Ch3[VCS], Ch4[IOUT]
1.0us/div
100ms/div

## Slide 13: OCP[ODSP]
Test Results
OCP is triggered with just one pulse.
JFET regulation is operated well.
Ch1[VGATE],,Ch2[VCS], Ch3[VIN], Ch4[IOUT]
Test condition: Vin[265Vac], CCOMI[2.2uF], CVDD[10uF]. Csn[20nF], Rsn[100k]
1.0us/div
100ms/div
VJFET.HL : 19V
VJFET.LL : 13V

## Slide 14: OVP – VDD and VS
Test Results
After LED opened, VDD OVP is triggered at 24.8V.
VS OVP is also triggered at 3.1V after LED opened.
Test condition: CCOMI[2.2uF], CVDD[10uF].
VDD OVP
VS OVP
VDD: 24.8V
LED Open
Ch1[VGATE],,Ch2[VDD], Ch3[VVS], Ch4[IOUT]
VVS: 1.56V
VDD: 17.3V
LED Open
VVS: 3.1V

## Slide 15: OVP – VDD and VS
Test Results
JFET regulation is operated well.
Test condition: CCOMI[2.2uF], CVDD[10uF].
Ch1[VGATE],,Ch2[VDD], Ch3[VVS], Ch4[IOUT]
VJFET.HL : 19V
VJFET.LL : 13V

## Slide 16
2. System
1) CC
2) THD/PF
3) Overshoot
4) Startup

## Slide 17: CC
±1.05%
Test results
Test condition: RVS1[200k], RVS2[30k], COUT[470uF], CCOMI[2.2uF]
 | 265Vac[50Hz] | 230Vac[50Hz] | 180Vac[50Hz] | 140Vac[60Hz] | 120Vac[60Hz] | 90Vac[60Hz]
Rcomp[200Ω] | ±1.02% | ±0.88% | ±1.18% | ±1.19% | ±1.04% | ±1.19%
Rcomp[220Ω] | ±1.78% | ±1.48% | ±1.33% | ±1.34% | ±1.19% | ±1.49%
±0.59%
Rcomp[200Ω]
Rcomp[220Ω]

## Slide 18: CC
Test results
Test condition: RVS1[200k], RVS2[30k], COUT[470uF], CCOMI[2.2uF]
±0.59%
EVT0
EVT1
Load regulation of EVT1 is having different pattern a little from EVT0.
±0.6%

## Slide 19: THD and PF
Samples | Io [mA] |  | PF |  | THD[%] | 
 | 90Vac | 265Vac | 90Vac | 265Vac | 90Vac | 265Vac
#01 | 336 | 339 | 0.997 | 0.904 | 3.65 | 7.73
#02 | 334 | 335 | 0.997 | 0.901 | 3.53 | 7.96
Test results
Test condition: CCOMI[2.2uF]
Vin[90Vac]
Vin[265Vac]
Ch3[VIN], Ch4[IIN]

## Slide 20: Overshoot
Vin level is detected by Ivs and VCOMI is charged by VCOMI modulator output.
VCOMI modulator output is inversely proportional to Vin level.
Therefore, VCOMI is adjusted close to steady state level during softstart time.
Concept

## Slide 21: Overshoot – 8.4W
Test Results
VCOMI clamped at startup is inverse proportional to Vin level and operated well.
 There are no overshoot even fast On & OFF of AC power.
Vin[90Vac]
Vin[265Vac]
Vin[277Vac]
VCOMI_INT.CLP: 2.1V
VCOMI_INT.CLP: 1.1V
Test condition: CCOMI[2.2uF], CVDD[10uF], CVDD[470uF], Lm[1mH].
Ch1[VDD],, Ch2[VIN], Ch3[VCOMI], Ch4[IOUT]
VCOMI_INT.CLP: 1.5V

## Slide 22: Startup time
Test Results
Startup time can meet 0.2s.
Test condition: Vin[90Vac], COUT[470uF], CCOMI[2.2uF], Lm[1mH]
Rstr: 30kΩ
178ms
Ch1[VDD],, Ch2[VIN], Ch3[VOUT], Ch4[IOUT]

## Slide 23
Follow us on Twitter @ twitter.com/fairchildSemi
View product and company videos, listen to podcasts and comment on our blog @ www.fairchildsemi.com/engineeringconnections
Visit us on Facebook @ www.facebook.com/FairchildSemiconductor