## Slide 1: Great Power Microelectronics Corp.
CMC 60W LED驱动电源方案
2014.07.21

## Slide 2
CU6503AN 60W应用方案概述
CU6503AN 60W Demo 相关参数资料
CU6503AN 60W 应用方案优势比对
CU6503AN 应用总结
总结
CMC 60W LED驱动电源方案

## Slide 3
CCM模式
效率：92%
PFC：0.95
THD：10
60W 应用方案概述
BOM：20RMB
Ipk<1.4 倍DC电流输出
变压器/MOS应力小
EMI容易通过
电源设计简单
PFC、THD无须环路调节

## Slide 4
60W Demo 相关参数资料
60W 应用方案原理图

## Slide 5
60W Demo 相关参数资料

## Slide 6: Test Report
40V1.5A POWER TEST DATA |  |  |  |  |  | 
Vin(Vac) | Pin(W) | PF | Vout(Vdc) | Iout(A) | Eff(%) | THD
110 | 67.420 | 0.9931 | 40 | 1.494 | 88.64% | 5.16
115 | 67.690 | 0.9925 | 40 | 1.502 | 88.76% | 
230 | 65.590 | 0.9428 | 40 | 1.484 | 90.50% | 
264 | 64.910 | 0.9099 | 40 | 1.469 | 90.53% | 14.25
Average | 66.154 |  |  | 1.487 | 89.60% | 
Accuracy | 1.50% | Line regulation |  | 2.43% |  | 

## Slide 7
7
Transformer Design

## Slide 8
60W Demo 相关参数资料

## Slide 9
CU6503AN功能
  Fast start-up (<0.3S)
Built-in HV Start Up
  Universal input without HV E-cap (longer life, lower cost)
  High PF (>0.95) & Low THD (<10%) to meet regulatory
Single stage PFC + PWM
  Lower peak current & Smaller Transformer (Lower Cost)
  Can use lower current rating MOSFET(Lower Cost)
  Less EMI suppression needed (Lower cost)
CCM Mode with
Internal Soft-Start
  No need LED Vf & IV binning
  Minimize impact of Vf change
CC+CP
  No need opto-coupler
Precision PSR (+/-2.5%)
  No need MOV or only lower rating MOV required
  Reliable
UVP & OVP Short & Open Protection
  Simple magnetic design
  Minimum EMI suppression
Fixed Frequency
  Lower material and assembly cost
Minimum external component

## Slide 10
CU6503AN CCM解读
Lesser component
Lower peak current
Lower Current MOS
Cost down
Smaller transformer
Better EMI

## Slide 11
CU6503AN内部设计原理
Pin = Constant for Constant Power (CP) LED
or
Pin = Vcc x Constant for CP + Constant Current (CC) LED
Pin = LED x Constant for CC LED
Pin = Vin x Iin
Pin = Vin x Imul x Constant
Pin = Vin x Constant x Iac x Vcc / (constant x Vrms x Vrms)
Pin = Vin x Vin x Vcc x Constant / (Vin x Vin)

## Slide 12
60W 应用方案优势比对
CU6503AN SY5800比对
A 60W
A 2PCS共模
A MOS 10A 650V
A 变压器没有屏蔽
B
A
B 45W
B 3PCS共模
B MOS 12A 650V
B 变压器有屏蔽
同款变压器比较：
PQ2620
A：CU6503AN
B：SY5800

## Slide 13
PQ2620变压器
10A650V MOSFET
EMI只需2PCS共模
过浪涌3000V
过雷击6000V
CU6503AN 应用总结

## Slide 14
BOM COST
SIMPLE
DIFFERENT
RELIABLE
FUTURE
CMC 设计理念

## Slide 15
谢谢！