## Slide 1
公司簡介 & 产品介绍
深圳市因斯达半导体有限公司
EAST SEMICONDUCTER TECHNOLOGY CO.,LTD
Make by Bruce
2016/06/21

## Slide 2
EST(East Semiconductor Technology Co., Ltd.)创立于1999年，专业从事电源类集成电路的设计、开发、制造和销售，产品主要应用于PC电源、适配器、充电器、LED电源和通讯模块电源等领域。
EST由一批中国内地和台湾的IC资深设计人员和产品应用工程师创立，在台湾建立了设计中心，内地分别设立了营运中心、IC测试厂、销售公司。长期合作商为台湾的台积电、联电、台湾光罩；封装厂为南通富士通、江阴长电、天水华天、西安微电等高品质封装厂，提供了完善的质量控制保证体系，形成了良好的销售和客户服务链。
EST凭借其在业界领先的产品设计能力及高品质封装、测试技术及良好的产品应用能力，竭诚为客户提供高性价比的产品，帮助客户降低生产成本和提升产品品质。
EST在中国深圳设立了深圳市因斯达半导体有限公司，承担EST产品在中国大陆的销售和应用服务。
公司簡介

## Slide 3
公司宗旨
诚信—笃守信誉、忠诚服务、互信互利；
创新—创新产品、创新市场、持续成长；
卓越—追求品质、技术、服务、成本之卓越；
共享—与客户、员工、股东共同发展，与社会共享.
誠信
創新
卓越
共享

## Slide 4
产品分类
AC/DC Converter
PC SPS Supervisor
基準IC
DC-DC Conveter
USB智能充電識別
MOS FET
OP比較器

## Slide 5
AC/DC Converter(1/3)
SSR控制芯片 |  |  |  |  |  |  |  |  | 
Part No. | Start-UP (µA) | UVLO OFF (V) | Switching Freq.(kHz) | Package | Freq. Shuffling | LEB(nS) | Application | Function | Cross Reference
EST UC2842A/AS | 500 | 16 / 10 | 52kHz | DIP8/SOP8 | N | 150 | PC / Adapter |  | UC3842
EST UC3842A/AS | 500 | 16 / 10 | 52kHz | DIP8/SOP8 | N | 150 | PC / Adapter |  | UC3842
EST UC2843A/AS | 500 | 7.8 / 7 | 52kHz | DIP8/SOP8 | N | 150 | PC / Adapter |  | UC3843
EST UC3843A/AS | 500 | 7.8 / 7 | 52kHz | DIP8/SOP8 | N | 150 | PC / Adapter |  | UC3843
EST UC2845A | 500 | 7.8 / 7 | 52kHz | DIP8/SOP8 | N | 150 | PC / Adapter |  | UC3845
EST UC3845AS | 500 | 7.8 / 7 | 52kHz | DIP8/SOP8 | N | 150 | PC / Adapter |  | UC3845
EST2263S | 10 | 14 / 9 | Adj. | SOP8 | Y | 300 | Charger / Adapter |  | OB2263
EST2263A | 10 | 14 / 9 | Adj. | SOP8 | Y | 300 | Charger / Adapter |  | OB2263
EST2800A | 8 | 13.5 / 7.5 | 65kHz | SOT23-6 | Y | 220 | Charger / Adapter / TV | OCP / OVP / OTP | OB2273 / LD5530
EST2800H | 8 | 13.5 / 7.5 | 135kHz | SOT23-6 | Y | 220 | Charger / Adapter / TV | OCP / OVP / OTP | LD5533
EST2900A | 4.5 | 20 / 7.5 | 65kHz | SOT23-6 | Y | 300 | Charger / Adapter / TV | OCP / OVP | OB2281
EST2900B | 4.5 | 20 / 7.5 | 65kHz | SOT23-6 | Y | 300 | Charger / Adapter / TV | OCP / OVP | 
EST2269S | 3(HV Start) | 16.5 / 10 | Adj. | SOP8 | Y | 250 | Charger / Adapter / TV |  | OB2269
EST2269A | 3(HV Start) | 16.5 / 10 | Adj. | DIP8 | Y | 250 | Charger / Adapter / TV |  | OB2269
PSR控制芯片 |  |  |  |  |  |  |  |  |  | 
Part No. | UVLO OFF (V) | Package | Power Switch | Cable Compen-sation | Application | Standby Power | Switching Freq.(kHz) | Freq. Shuffling | Function | Cross Reference

## Slide 6
AC/DC Converter(2/3)
SSR內包MOS控制芯片 |  |  |  |  |  |  |  |  |  | 
Part No. | Standby Power | UVLO OFF (V) | RDS (on) | MOSFET | Switching Freq.(kHz) | Package | Freq. Shuffling | Application | Function | Cross Reference
EST2810H | <70mW | 13.5 / 7.5 | 9 | 650V | 135kHz | DIP7 | Y | Charger / Adapter | OCP / OVP / OTP | 
EST2812A | <70mW | 13.5 / 7.5 | 4 | 650V | 65kHz | DIP7 | Y | Charger / Adapter | OCP / OVP / OTP | 
EST2915H | <50mw | 20 / 7.5 | 2.2 | 700V | 135kHz | DIP7 | Y | Charger / Adapter | OCP / OVP / OTP | 
EST2920A | <50mw | 20 / 7.5 | 2.2 | 700V | 65kHz | DIP7 | Y | Charger / Adapter | OCP / OVP / OTP | 
EST2925H | <50mw | 20 / 7.5 | 2.2 | 700V | 135kHz | DIP7 | Y | Charger / Adapter | OCP / OVP / OTP | 
EST2930A | <50mw | 20 / 7.5 | 1.6 | 700V | 65kHz | DIP7 | Y | Charger / Adapter | OCP / OVP / OTP | 
PSR內包MOS控制芯片 |  |  |  |  |  |  |  |  |  | 
Part No. | Standby Power | UVLO OFF (V) | RDS (on) | Switching Freq.(kHz) | Package | Freq. Shuffling | LEB(nS) | Application | Function | Cross Reference
EST2605A | <70mW | 10.8 / 6.8 | 18Ω | 65KHz | SOP8 | Y | 5W Charger / Adapter | CV/CC ±5% | OB2535 | EST2605A

## Slide 7
PC SPS Supervisor
PC SPS Supervisor |  |  |  |  |  |  |  |  |  | 
Part No. | Category | OVP | UVP | OCP | OTP | BNO | FC | TL431 | Package | Cross Reference
EST7502C | 3.3V/5V/12V | 3.3V/5V/12V | 3.3V/5V/12V | NA | NA | NA | NA | NA | DIP16 | SDC2921 / WT7520 / HS8110
EST6105A | 3.3V/5V/12V | 3.3V/5V/12V | 3.3V/5V/12V | NA | NA | NA | NA | NA | DIP20 | SG6105 / HS8108
EST7610B | 3.3V/5V/12V | 3.3V/5V/12V | 3.3V/5V | NA | NA | NA | NA | NA | DIP8 /SOP8 | WT7510
EST7618A | 12Va/12Vb | 12Va/12Vb | 12Va/12Vb | 12Va/12Vb | NA | NA | NA | NA | DIP8 /SOP8 | WT7618
EST7627A | 3.3V/5V/12Va/12Vb | 3.3V/5V/12Va/12Vb | 3.3V/5V/12Va/12Vb | 3.3V/5V/12Va/12Vb | NA | NA | NA | NA | DIP16 / SOP16 | WT7627
EST7630A | 3.3V/5V/12Va/12Vb | 3.3V/5V/12Va/12Vb | 3.3V/5V/12Va/12Vb | 3.3V/5V/12Va/12Vb | NA | NA | NA | NA | DIP14 / DIP16 /DIP20 | WT7525 / PS224

## Slide 8
基準IC & DC-DC & OP amp & 智能充電識別
基準IC |  |  |  |  |  |  |  |  |  |  | 
Part No. | VKA(V) | IKA(mA) | Vref | ∆Vref | ∆Vref /∆VKA | Iref | ∆Iref | IKA(min) (mA) | IKA(OFF) (nA) | ZKA | Package
EST TL431AL | 36 / Vref | 100 / 1 | 2.488 / 2.5 / 2.512 | 3 | 1.4 | 1.8 | 0.4 | 0.27 | 260 | 0.22 | TO-92
EST TL431AJ | 36 / Vref | 100 / 1 | 2.488 / 2.5 / 2.512 | 3 | 1.4 | 1.8 | 0.4 | 0.27 | 260 | 0.22 | SOT23
EST TL431BL | 36 / Vref | 100 / 1 | 2.475 / 2.5 / 2.525 | 3 | 1.4 | 1.8 | 0.4 | 0.27 | 260 | 0.22 | TO-92
EST TL431BJ | 36 / Vref | 100 / 1 | 2.475 / 2.5 / 2.525 | 3 | 1.4 | 1.8 | 0.4 | 0.27 | 260 | 0.22 | SOT23
EST TL432AL | 12 / Vref | - | 1.234 / 1.24 / 1.246 | 3 | 1.4 | 1.8 | 0.4 | 0.27 | 260 | 0.22 | TO-92
EST TL432AJ | 12 / Vref | - | 1.234 / 1.24 / 1.246 | 3 | 1.4 | 1.8 | 0.4 | 0.27 | 260 | 0.22 | SOT23
EST TL432BL | 12 / Vref | - | 1.228 / 1.24 / 1.252 | 3 | 1.4 | 1.8 | 0.4 | 0.27 | 260 | 0.22 | TO-92
EST TL432BJ | 12 / Vref | - | 1.228 / 1.24 / 1.252 | 3 | 1.4 | 1.8 | 0.4 | 0.27 | 260 | 0.22 | SOT23
DC-DC |  |  |  |  |  |  | 
Part No. | Switching Freq.(kHz) | Ichg | Idischg | VIPK | VFB | ICC | Package
EST MC34063 | 33kHz | 35uA | 220uA | 300mV | 1.25V | 2.75mA | DIP8
EST MC34063S | 33kHz | 35uA | 220uA | 300mV | 1.25V | 2.75mA | SOP8
OP比較器 |  |  |  |  | 
Part No. | Bias Current | Offset Voltage | Offset Current | Saturation Voltage | Package
EST LM339 | 25nA(Typ) | ±2.0mV(Typ) | ±5.0nA(Typ) | 130mV(Typ) @ 4.0mA | DIP14/SOP14
EST LM393 | 25nA(Typ) | ±1.0mV(Typ) | ±5.0nA(Typ) | 150mV(Typ) @ 4.0mA | DIP8/SOP8
EST LM258 | -20nA(Typ) | 3.0mV(Typ) | 2.0nA(Typ) | - | DIP8/SOP8
EST LM358 | -20nA(Typ) | 3.0mV(Typ) | 2.0nA(Typ) | - | DIP8/SOP8
USB智能充電識別 |  |  |  |  | 
Part No. | Supports |  |  |  | Package
EST5181 | E-Marker |  | USB 3.1 3A current |  | SO-23-5
EST5192 | Type-c PD |  | USB Type-C DFP CC & PD Controller |  | SOP16/DFN
EST5198B | Samsung | BC1.2 | selectable Apple 1A ,2A and 2.4A | Single | SO-23-5
EST5199B | Samsung | BC1.2 | selectable Apple 1A ,2A and 2.4A | Dual | SO-23-6
EST5298A | QC2.0 | BC1.2 | Apple 2.1A and 2.4A |  | SOP8
EST5398 | QC3.0 |  | QC2.0、BC1.2、FCP |  | SOP-8

## Slide 9
LV/HV MOSFET & Super Junction MOSFET
HV MOS FET |  |  |  |  |  |  |  |  |  | 
Part No. | Ch. | VDS | VGS | ID | RDS(on) Max. Ω | Ciss Typ. | VGS(th) Max. | QgTyp. Nc | PD | Package
EST02N60 | N | 600V | 4.5V | 2.0A | 4.6 | 320pF | ±30V | 3.5nc | 23W | TO-220F
EST04N60 | N | 600V | 4.5V | 4.5A | 2.6 | 600pF | ±30V | 3nc | 44W | TO-220F
EST06N60 | N | 600V | 4.5V | 6.0A | 2.5 | 870pF | ±30V | 4.5nc | 54W | TO-220F
EST07N60 | N | 600V |  |  | 1.3 |  |  |  |  | TO-220F
EST08N60 | N | 600V | 4.5V | 7.5A | 1.2 | 1200pF | ±30V | 6.5nc | 48W | TO-220F
EST10N60 | N | 600V | 4.5V | 9.5A | 0.8 | 1600pF | ±30V | 9nc | 50W | TO-220F
EST02N65 | N | 650V |  |  | 4.6 |  |  |  |  | TO-220F
EST04N65 | N | 650V |  |  | 2.6 |  |  |  |  | TO-220F
EST06N65 | N | 650V |  |  | 2.5 |  |  |  |  | TO-220F
EST07N65 | N | 650V |  |  | 1.3 |  |  |  |  | TO-220F
EST08N65 | N | 650V | 4.5V | 7.5A | 1.16 | 1200pF | ±30V | 6.5nc | 48W | TO-220F
EST10N65 | N | 650V | 4.5V | 9.5A | 0.8 | 1600pF | ±30V | 9nc | 50W | TO-220F
EST11N65 | N | 650V |  |  |  |  |  |  |  | TO-220F
EST11N90 | N | 900V |  |  |  |  |  |  |  | TO-220F
EST13N50 | N | 900V |  |  |  |  |  |  |  | TO-220F
EST18N50 | N | 900V |  |  |  |  |  |  |  | TO-220F
EST21N65 | N | 900V |  |  |  |  |  |  |  | TO-220F
LV MOS FET |  |  |  |  |  |  |  |  |  | 
Part No. | Ch. | VDS | VGS | ID | RDS(on) Max.mΩ | Ciss Typ. | VGS(th) Max. | QgTyp. Nc | PD | Package

## Slide 10
Schottky
Schottky |  |  |  |  |  | 
Part No. | VRRM Max. | IF | IFSM | VF@IF Max. |  | Package
 | V | A | A | V | mA | 
MBR2045CT | 45 | 20 | 150 | 0.6 | 0.05 | TO-220/TO-220F
MBR2065CT | 65 | 20 | 150 | 0.7 | 0.05 | TO-220/TO-220F
MBR3045CT | 45 | 30 | 150 | 0.6 | 0.2 | TO-220/TO-220F
MBR3065CT | 65 | 30 | 150 | 0.7 | 0.2 | TO-220/TO-220F
MBR10100CT | 100 | 10 | 120 | 0.82 | 0.05 | TO-220/TO-220F
MBR10150CT | 150 | 10 | 120 | 0.84 | 0.05 | TO-220/TO-220F
MBR10200CT | 200 | 10 | 120 | 0.85 | 0.05 | TO-220/TO-220F
MBR20100CT | 100 | 20 | 150 | 0.85 | 0.05 | TO-220/TO-220F
MBR20150CT | 150 | 20 | 150 | 0.95 | 0.1 | TO-220/TO-220F
MBR20200CT | 200 | 20 | 150 | 0.93 | 0.2 | TO-220/TO-220F
MBR30100CT | 100 | 30 | 150 | 0.85 | 0.2 | TO-220/TO-220F
MBR30150VT | 150 | 30 | 150 | 0.88 | 0.2 | TO-220/TO-220F
MBR30200CT | 200 | 30 | 150 | 0.95 | 0.2 | TO-220/TO-220F
EST10L45S | 45 | 10 | 120 | 0.53 | 0.4 | TO-277
EST20L45 |  |  |  |  |  | TO-220/TO-220F

## Slide 11
感谢你的聆听
LOGO