## Slide 1
EUTECH high-end Car charger solution:
EUP3467 5V/3.4A
2014-07

## Slide 2: Agenda
1.High-End car charger requirements
2.EUP3466/7 features
3.EUP3466 5V/2.4A application circuit & PCBA picture
4.EUP3466 efficiency
5.EUP3466 CC precision data
6.EUP3466/7 SCP waveform
7.EUP3466 5V/2.4A BOM
8.EUP3467 5V/3.4A application circuit & PCBA picture
9.EUP3467 efficiency
10.EUP3467 CC precision data
11.EUP3467 5V/3.4A BOM
12.EUP3467 5V/3.4A EMI data
13.EUP3466/7 Layout guide

## Slide 3
Input voltage max. 40V
Input under voltage protection
CC precision:≤±6%
CV precision
Cable compensation
Output OVP
EMI
High-End car charger requirements

## Slide 4: EUP3466/7 A features
Input voltage:8V – 36V,max. 40V
Fixed 80kHz Switching Frequency
CV precision:±1%
CC precision:±4%
Programmable Cable compensation (max. 0.6V)
Output OVP programmable
Fold-back short circuit protection
Thermal shutdown
SOP-8(EP) package

## Slide 5
EUP3467 5V/3.4A application circuit

## Slide 6: EUP3467 efficiency
Vin(V) | Iin(A) | Vout(V) | Iout(A) | Eff.(%) | IC表面温度(Ta=26℃)
12.16 | 0.0033 | 5.16 | 0 |  | 
24.13 | 0.0018 | 5.16 | 0 |  | 
28.87 | 0.0016 | 5.16 | 0 |  | 
12.35 | 1.665 | 5.33 | 3.4 | 88.13% | 
24.13 | 0.854 | 5.33 | 3.4 | 87.94% | 92.6 ℃
28.88 | 0.715 | 5.33 | 3.4 | 87.76% | 98.2 ℃
1.线损补偿:△V=5.27uA*Iout*R3*R4=5.33V-5.16V=0.17V

## Slide 7: EUP3467 CC precision data
Vin(V) | Iin(A) | Vout(V) | Iout(A)
12.36 | 1.06 | 2.833 | 3.715
12.33 | 1.4 | 3.98 | 3.681
12.31 | 1.69 | 4.94 | 3.673
24.18 | 0.54 | 2.8 | 3.681
24.16 | 0.73 | 4.05 | 3.661
24.15 | 0.87 | 5 | 3.656
1.恒流精度:(3.715-3.66)/3.66*100%=1.5%

## Slide 8: EUP3466/7 SCP waveform
CH1:SW,CH2:Vout,CH4:Iin
1.EUP3466/7 输出短路后进入打嗝模式, T=2s
输出短路时输入的平均电流很小:小于0.1A

## Slide 9
EUP3467 5V/3.4A BOM
序号 | 类别 | 封装 | 规 格 | 厂 商 | 单位 | 用量
R1 | 贴片电阻 | 0603 | 100k 5% |  | 个 | 1
R2 | 贴片电阻 | 1210 | 47mR 1% |  | 个 | 1
R3 | 贴片电阻 | 1210 | 0.1R 1% |  | 个 | 1
R4 | 贴片电阻 | 0603 | 330k 1% |  | 个 | 1
R5 | 贴片电阻 | 0603 | 100K 1% |  | 个 | 1
R6 | 贴片电阻 | 0603 | 1.2k 1% |  | 个 | 1
R7 | 贴片电阻 | 0603 | 330R 1% |  | 个 | 1
R9,R15 | 贴片电阻 | 0603 | 75k 1% |  | 个 | 2
R11,R13 | 贴片电阻 | 0603 | 43.2k 1% |  | 个 | 2
R10,R12,R14,R16 | 贴片电阻 | 0603 | 49.9k 1% |  | 个 | 4
R8 | 贴片电阻 | 0603 | 1k 5% |  | 个 | 1
C1,C7 | 贴片陶瓷电容 | 0603 | 100nF/50V X5R |  | 个 | 2
C2 | 贴片陶瓷电容 | 0603 | 47nF/25V X5R |  | 个 | 1
C3,C5 | 贴片陶瓷电容 | 0603 | 47pF/25V X5R |  | 个 | 2
EC1 | 电解电容,Low ESR | 6.3*5 | 100uF/35V |  | 个 | 1
EC2 | 电解电容,Low ESR | 6.3*5 | 220uF/10V |  | 个 | 1
U1 | EUP3466 | SOP8-EP | Car charger IC | EUTECH | 个 | 1
L1 | 铁硅铝环电感 | 6*13 | MC044125A-68uH 0.7线径 | 美创电感 | 个 | 1
D1 | 肖特基 | TO-277 | SL10U50P | Motive | 个 | 1
LED1 | 贴片LED | 0603 |  |  | 个 | 1
F1 | 贴片保险丝 | 0805 | 2.5A |  | 个 | 1

## Slide 10
EUP3467 5V/3.4A EMI data(方案一)
对策一: Bead+Snubber
输入: 24V VIN
参数: Bead=30R/100M; R=15R; C=2.2nF
Margin:vertical=-7.88dB; Horizontal=-4.57dB

## Slide 11
EUP3467 5V/3.4A EMI data (方案一)
对策一: Bead+Snubber
输入: 12V VIN
参数: Bead=30R/100M; R=15R; C=2.2nF
Margin:vertical=-9.69dB; Horizontal=-11.93dB

## Slide 12
EUP3467 5V/3.4A EMI data (方案二)
对策二: 只Snubber
输入: 12V VIN
参数: R=15R; C=2.2nF
Margin:vertical=-5.58dB; Horizontal=-2.30dB

## Slide 13
EUP3467 5V/3.4A EMI data (方案二)
对策二: 只Snubber
输入: 24V VIN
参数: R=15R; C=2.2nF
Margin:vertical=-5.47dB; Horizontal=-4.96dB

## Slide 14
EUP3466/7 Layout guide
1. VIN、GND、SW、VOUT 等功率线，铜箔走线粗、短、直；
2. FB/OVEN /COMP/SENSE走线远离电感与肖特基等开关信号地方,最好能使用地线包围；
3. 输入电容靠近芯片VIN 与GND 引脚,尤其0.1uF滤波电容尽量靠芯片引脚放置.
4. SW需要铺一定面积的铜箔, 提高芯片的散热效率.
5.FB/OVEN走线从输出滤波电容后引出, 走线短.
6.肖特基GND端走线与输入电容连接,输入端地与输出端地单点连接